Park-it-CDA

---
Team
Nikolai
  - Mesh Networking
Tyrel
  - Simulation
  - Database
Zane
  - Unit design
  - Sensor prototyping

---
Requirements
5 Units
1 year battery life
Sense obstacle
Indicate blockage
Mesh network
Auto choose gateway
Report state changes
Simulate the rest of garage

---
Schedule

---
Assumptions
We assume that LoRa will have the distance capabilities to reach the den.
We assume that we can achieve everything on a 3.3v system.
We assume that we can survive for a year on a 10000 mAh battery utilizing deep sleep.

---
Issues
The battery life will be the bottleneck.
  - With a 3.7% PWM duty cycle on an arduino mega we can run the led for approximately 235 days with a 10000 mAh battery.
  - We assume that with a few solar panels we could extend the battery life to allow for a full year even with indirect lighting.
  - We could also blink the LED at regular intervals instead of having them on all the time. This requires timing between units.
  - We still need to allow for the networking.

---
Context Diagram

---
Context Diagram

---
Context Diagram

---
Impacted Modules
We could purchase an off the shelf Arduino MKR 1310 which has a built in hardware encryption chip and 107uA deep sleep with built in LoRa.
We would be relying on the open source LoRa libraries for our communication packages, and an open source package for the discreet simulator.

---
Three Prototype Test Cases
Sensor
  - Identify a car, truck, and possibly a motorcycle
Network
  - Mesh communication
  - External reporting
Simulation
  - How do we test the simulation????

---
Traceability Approach
"the ability to describe and follow the life of a requirement in both a forwards and backwards direction (i.e., from its origins, through its development and specification, to its subsequent deployment and use, and through periods of ongoing refinement and iteration in any of these phases)"
We need to develop a way to show how this works.

---
Schedule

---
Current Status – LoRa Testing
We have received hardware and have tested the viability of using LoRa and Arduino
Test conditions:
  - 3 Arduino Uno/Mega with a LoRa radio attached – A Garage Sensor Unit (GSU)
  - Used the LoRa mesh network implementation at https://github.com/nootropicdesign/lora-mesh
  - Broadcasts at maximum power – 100mA per transmission
  - This implementation periodically sends messages including the Received Signal Strength Indicator (RSSI) of each radio in the network
  - Placed one GSU by the entrance to UofI’s office at the Den
  - Using a laptop and console, measure how far another GSU can be before connection drops out (Goal is to get to the garage ~400 ft away)

---
Current Status – LoRa Testing
When next to one another, RSSI is 0 to -60
As soon as we leave the Den, RSSI dropped to -90 – the brick construction of the Den is causing a large loss of signal strength
The signal completely drops out at -120 – halfway between the Den and the traffic lights on 4th (approx 120 ft)

---
Current Status – LoRa Testing

---
Current Status – LoRa Testing
Carpark Testing
  - Stand by the entrance and Tyrel walks with one of the GSUs
  - Signal strength varies between -90 and -120 RSSI as Tyrel walks around and up the garage levels
  - Connection drops out once as Tyrel is at the farthest corner from us on the second floor
  - Typical RSSI was -100 to -110
Reaching the garage from the Den when outdoors
  - Walked back to the Den while monitoring RSSI
  - We get to the Den and stand below where the weather station above the Den is
  - RSSI without LOS is about -100 to -110

---
Current Status – LoRa Testing

---
Current Status – LoRa Testing
Overall Conclusion
  - LoRa will work within the garage and will be able to communicate with a GSG on top of the Den if we have line of sight
  - We need to test lower power output on the LoRa radios to preserve battery
Concerns
  - The mesh network implementation uses 1400 bytes of RAM: ~70% of what’s available on the Arduino Uno/Pro Mini and 40% of the available FLASH. We may not have enough RAM for our implementation along with the sensing on a Pro Mini.

---
Action Items
Intentionally left blank.