## Slide 1: Park – It - Cda
A Garage sensor system over a mesh network

## Slide 2: Park – it - cda
Team members and roles
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site

## Slide 3: Value proposition
The problem
Too much time and effort are being spent by those looking for a place to park in one or more garages in downtown Coeur d’ Alene.
Our solution
A parking indication system
Vehicle sensing over stalls
LED indication to commuters
Mesh networking via detection/indication units

## Slide 4: Objective and deliverables
Our goal
Outfit the parking garage in downtown CDA with 5 prototype units
Build a mesh network for units to relay stall status to a gateway at the Innovation Den
Build a simulation to show what a full-garage deployment would look like

## Slide 5: Requirements
The units | The mesh network | The simulation
Enclosure no larger than 4” X 4” X 4” | Units relay messages to gateway at the den | representation of a full garage deployment
Sensors to detect presence of vehicles in stall | Data maintains integrity and authentication | Real time updates of stall status
Must last at least a year via battery power | Units are provisioned | Populated with accurate test data
LED to indicate stall status to commuters | Units are synchronized and can communicate with each other for message routing | Expandable for future projects
The units | The mesh network | The simulation
Redundancies of sensors for better accuracy | Units can choose a master and slave dynamically to save on battery | Graphical representation of system
Solar panels | Encryption of data | Companion app for phone/tablet
Security camera-like appearance for theft/tamper prevention |  | Data collection
Optional features

## Slide 6: Components and mediums
The hardware
The Board
The Sensors
Other Components
Adafruit Feather M0 LoRa
RGB LED
AM312 PIR Sensor
HC-SR04 Ultrasonic Sensor
Locking Power Switch
Real-Time Clock
2500mah Lipo Battery
LoRa Antenna
Lipo Charger

## Slide 7: Sensing vehicles
- The ultrasonic sensor reads the distance to the ground 3 times to see if there is a blockage in the stall, outlying distances are thrown out in a 2 – to – 1 vote
A combination of sensors are used to detect the presence of a vehicle
- The PIR sensor wakes up the CPU via external interrupt when a heat signature (vehicle) is detected below
- The processor changes the LED from green (vacant) to red (full)
- Stall status is sent periodically to the gateway over LoRa transmission

## Slide 8
Stay at home testing
Sensing vehicles

## Slide 9: The Enclosure
Designing and 3d printing
Final enclosure design, created in Fusion360
Full assembly of working prototype
Copper PIR limiter
LED diffuser
Access to CPU and Lipo Underneath

## Slide 10: Nikolai mesh networking
LoRa
LoRa (Long Range) was selected due to its ability to transmit over a long-range and low power usage
Create a mesh network where each of the 5 Garage Sensor Units (GSU) can communicate with one another, later changed to a star with one GSU a Garage Sensor Master (GSM)
The GSM would receive messages from the GSUs and then send data to the Garage Sensor Gateway (GSG) at the Innovation Den

## Slide 11: Nikolai mesh networking
LoRa
Our testing revealed that we will be able to make the distance between the parking garage and the roof of the Innovation Den approx. 350 ft apart.

## Slide 12: Tyrel Simulation

## Slide 13: Joel Encryption
Encryption
A class was created to send and receive crypted data throughout the network. This
class implements private key cryptography.
      Two private keys and a predetermined pattern are used to encrypt and decrypt data
      Encryption method
      Methods to access or print the original and crypted data

## Slide 14: Joel Encryption
Font 48 for headlines
Font 36 for lists and other txt
WIKI

## Slide 15: Covid-19 update
Our efforts to test and communicate while staying at home
Being a collaborative group, with each portion of our project communicating together dynamically, the “stay at home” order greatly affected our project
We could no longer be in the same location
The garage we planned to deploy our prototypes in was unavailable
We needed a way to communicate and test our units while remaining at home

## Slide 16: Lora stands for long range
Testing the capabilities of our transceiving medium
Dr. Shovic gave us 2 Yagi antennas used for extremely long range transmissions
The specs for the antenna are measured in line-of-sight conditions
We were hopeful that a house-to-house communication would be possible
Zane and Nikolai were the closest in proximity, being just over 1.2 miles apart
Nikolai uploaded some simple transceiver tests to the LoRa boards

## Slide 17: Testing long range
Makeshift masts and 3d printed hardware
Nikolai acquired a 20’ TV antenna, and turned it into a mast, attaching it to his flagpole
Zane designed some custom hardware for affixing a mast made from PVC to his roof

## Slide 18: Successful transmissions
There were several successful transmissions made and received between both Zane and Nikolai
However, many more packets were lost than were received

## Slide 19: Final setup
Something more reliable
In the end, the long-range communication just wasn’t stable and reliable enough for demonstration purposes
Our final setup for testing involves having the units, and the gateway at the same location
However, our testing has shown us that the units will be more than capable of transmitting messages from the parking the garage to the Innovation den once both have reopened and the project is able to be properly deployed

## Slide 20: Park – it - cda
Questions
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site