## Slide 1: Park – It - Cda
A Garage sensor system over a mesh network

## Slide 2: Value proposition
The problem
Too much time and effort are being spent by those looking for a place to park in one or more garages in downtown Coeur d’ Alene.
Our solution
A parking indication system
Vehicle sensing over stalls
LED indication to commuters
Mesh networking via detection/indication units

## Slide 3: Objective and deliverables
Our goal
Outfit the parking garage in downtown CDA with 5 prototype units
Build a mesh network for units to relay stall status to a gateway at the Innovation Den
Build a simulation to show what a full-garage deployment would look like

## Slide 4: Hard requirements
The units | The mesh network | The simulation
Enclosure no larger than 4” X 4” X 4” | Units relay messages to gateway at the den | representation of a full garage deployment
Sensors to detect presence of vehicles in stall | Data maintains integrity and authentication | Real time updates of stall status
Must last at least a year via battery power | Units are provisioned | Populated with accurate test data
LED to indicate stall status to commuters | Units are synchronized and can communicate with each other for message routing | Expandable for future projects
The units | The mesh network | The simulation
Redundancies of sensors for better accuracy | Units can choose a master and slave dynamically to save on battery | Graphical representation of system
Solar panels | Encryption of data | Companion app for phone/tablet
Security camera-like appearance for theft/tamper prevention |  | Data collection
soft requirements

## Slide 5: Park – it - cda
Team members and roles
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site

## Slide 6: deliverables
Chart: 
| Testing | Design | Documentation
Breakdown of work | 0.2 | 0.3 | 0.5

## Slide 7: planning
Selecting hardware and software
Board qualities
- Low current usage for active and idle
- Enough memory to handle Radiohead library and sensor libraries
- 3v3 Power supply to save battery
Sensors and LEDs
- Deep sleep modes
- Accuracy
- Can interrupt processor
Mediums
- RGB LEDs for ease and enclosure space
- Low power, high range communication protocol
- Lightweight simulation software

## Slide 8: Components and mediums
The hardware
The Board
The Sensors
Other Components
Adafruit Feather M0 LoRa
RGB LED
AM312 PIR Sensor
HC-SR04 Ultrasonic Sensor
Locking Power Switch
Real-Time Clock
2500mah Lipo Battery
LoRa Antenna
Lipo Charger

## Slide 9: Sensing vehicles
- The ultrasonic sensor reads the distance to the ground 3 times to see if there is a blockage in the stall, outlying distances are thrown out in a 2 – to – 1 vote
A combination of sensors are used to detect the presence of a vehicle
- The PIR sensor wakes up the CPU via external interrupt when a heat signature (vehicle) is detected below
- The processor changes the LED from green (vacant) to red (full)
- Stall status is sent periodically to the gateway over LoRa transmission

## Slide 10
Stay at home testing
Sensing vehicles

## Slide 11: The Enclosure
Designing and 3d printing
Final enclosure design, created in Fusion360
Full assembly of working prototype
Copper PIR limiter
LED diffuser
Access to CPU and Lipo Underneath

## Slide 12: Trials and lessons learned
Sensors and enclosure
- LEDs don’t have much spread
- PIR sensors can see everything
- Not all sensors are created equal

## Slide 13: Nikolai mesh networking
LoRa
LoRa (Longe Range) was selected due to its ability to transmit over a long-range -10’s of Kilometers in perfect conditions, and low power usage in sleep mode
Originally going to create a mesh network where each of the 5 Garage Sensor Units (GSU) can communicate with one another
The GSUs would determine amongst themselves one of them to become the Garage Sensor Master (GSM)
The GSM would receive messages from the GSUs and then send data over to the Innovation Den
Due to time limitations, the network was changed to become a star with a fixed GSM
Our testing revealed that we will be able to make the distance between the parking garage and the Innovation Den approx. 350 ft apart.

## Slide 14: Nikolai mesh networking
LoRa
Our testing revealed that we will be able to make the distance between the parking garage and the roof of the Innovation Den approx. 350 ft apart.

## Slide 15: BATTERY
Major requirement is to have every GSU in the parking garage last a full year without recharge
2 challenges posed here – Minimizing battery usage and procuring a large enough battery
Reducing battery usage involved selecting an Arduino based device and reduce power usage by putting it to sleep
Obtaining a battery from a reputable vendor proved to be a large time sink – ideal battery size ~20,000 mAh
Requirement changed to obtain a smaller battery due to difficulty in sourcing
Solar power was also something considered – use ambient light and a solar charger to provide a trickle charge

## Slide 16: Tyrel Simulation
Font 48 for headlines
Font 36 for lists and other text

## Slide 17: Joel Encryption
Encryption
A class was created to send and receive crypted data throughout the network. This
class implements private key cryptography.
      Two private keys and a predetermined pattern are used to encrypt and decrypt data
      Encryption method
      Methods to access or print the original and crypted data

## Slide 18: Joel Encryption
Font 48 for headlines
Font 36 for lists and other txt
WIKI

## Slide 19: Covid-19 update
Our efforts to test and communicate while staying at home
Being a collaborative group, with each portion of our project communicating together dynamically, the “stay at home” order greatly affected our project
We could no longer be in the same location
The garage we planned to deploy our prototypes in was unavailable
We needed a way to communicate and test our units while remaining at home

## Slide 20: Lora stands for long range
Testing the capabilities of our transceiving medium
Dr. Shovic gave us 2 Yagi antennas used for extremely long range transmissions
The specs for the antenna are measured in line-of-sight conditions
We were hopeful that a house-to-house communication would be possible
Zane and Nikolai were the closest in proximity, being just over 1.2 miles apart
Nikolai uploaded some simple transceiver tests to the LoRa boards

## Slide 21: Testing long range
Makeshift masts and 3d printed hardware
Nikolai acquired a 20’ TV antenna, and turned it into a mast, attaching it to his flagpole
Zane designed some custom hardware for affixing a mast made from PVC to his roof

## Slide 22: Successful transmissions
There were several successful transmissions made and received between both Zane and Nikolai
However, many more packets were lost than were received

## Slide 23: Final setup
Something more reliable
In the end, the long-range communication just wasn’t stable and reliable enough for demonstration purposes
Our final setup for testing involves having the units, and the gateway at the same location
However, our testing has shown us that the units will be more than capable of transmitting messages from the parking the garage to the Innovation den once both have reopened and the project is able to be properly deployed