## Slide 1: Park – It - Cda
A Garage sensor system over a mesh network

## Slide 2: Park – it - cda
Team members and roles
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site
1

## Slide 3: Value proposition
The problem
Too much time and effort are being spent by those looking for a place to park in one or more garages in downtown Coeur d’ Alene.
Our solution
A parking indication system
Vehicle sensing over stalls
LED indication to commuters
Mesh networking via detection/indication units
A dynamic companion webpage to monitor/simulate entire garage
2

## Slide 4: Objective and deliverables
Our goal
Outfit the parking garage in downtown CDA with 5 prototype units
Build a mesh network for units to relay stall status to a gateway at the Innovation Den
Build a simulation to show what a full-garage deployment would look like
3

## Slide 5: Requirements
The units | The mesh network | The simulation
 |  | Expandable for future projects
The units | The mesh network | The simulation
 | Units can choose a master and slave dynamically to save on battery | Graphical representation of system
Lasts at least a year via battery power | Encryption of data | Companion app for phone/tablet
Security camera-like appearance for theft/tamper prevention |  | Data collection
Optional features
Enclosure no larger than 4” X 4” X 4”
Sensors to detect presence of vehicles in stall
LED to indicate stall status to commuters
Units relay messages to gateway at the den
Data maintains integrity and authentication
Units are provisioned
Units synchronized and can communicate for message routing
Representation of a full garage deployment
Real time updates of stall status
Populated with accurate test data
Redundancies of sensors for better accuracy
4

## Slide 6: Components
The hardware
The Microcontroller
The Sensors
Other Components
Adafruit Feather M0 LoRa
Red/Green/Blue LED
AM312 PIR Motion Sensor
HC-SR04 Ultrasonic Distance Sensor
Latching Power Switch
Real-Time Clock
2500mah Lipo Battery
LoRa Antenna
Lipo Charger
Power
5

## Slide 7: The Enclosure
Prototyping, Designing and assembling
Final enclosure design created in Fusion360
Breadboard assembly
Real-time clock
LoRa antenna
Ultrasonic distance sensor
Feather M0 w/LoRa
RGB LED
Designing the enclosure
PIR sensor
6

## Slide 8: Completed prototype
- The ultrasonic sensor reads the distance to the ground 3 times to see if there is a blockage in the stall, outlying distances are thrown out in a 2 – to – 1 vote
- The PIR motion sensor wakes up the CPU via external interrupt when a heat signature (vehicle) is detected below
- The processor changes the LED from green (vacant) to red (full)
- Stall status is sent periodically to the gateway over LoRa transmission
- Additional design features include a power switch
- And access to the processor and battery underneath for charging and updating
7

## Slide 9
Stay at home testing
Sensing vehicles
- 3D printed PVC mount
8

## Slide 10: mesh networking
LoRa
LoRa (Long Range) was selected due to its ability to transmit over a long-range and low power usage
Create a mesh network where each of the 5 Garage Sensor Units (GSU) can communicate with one another, later changed to a star with one GSU a Garage Sensor Master (GSM)
The GSM would receive messages from the GSUs and then send data to the Garage Sensor Gateway (GSG) at the Innovation Den
9

## Slide 11: mesh networking
LoRa
Our testing revealed that we will be able to make the distance between the parking garage and the roof of the Innovation Den approx. 350 ft apart.
10

## Slide 12: Encryption
Encryption
A class was created to send and receive crypted data throughout the network. This
class implements private key cryptography.
      Two private keys and a predetermined pattern are used to encrypt and decrypt data
      Encryption method
      Methods to access or print the original and crypted data
11

## Slide 13: Encryption
(Example)
Client
Server
12

## Slide 14: Wiki
Highlights the major components and the team’s lessons that were learned during the entire process
Provides more detail and additional documentation about our project
http://mindworks.shoutwiki.com/wiki/Park-It-CdA:_Garage_Sensor_System_over_a_Mesh_Network
13

## Slide 15: Covid-19 update
Our efforts to test and communicate while staying at home
We are a collaborative group, that could no longer be in the same location
We needed a way to communicate and test our units while remaining at home
Our sponsor, Dr. Shovic, gave us 2 long-range Yagi antennas
Nikolai and Zane, being the closest in proximity, started testing house-to-house communication
14

## Slide 16: Testing long range
Makeshift masts and 3d printed hardware
Nikolai acquired a 20’ TV antenna, and turned it into a mast, attaching it to his flagpole
Zane designed some custom hardware for affixing a mast made from PVC to his roof
15

## Slide 17: Successful transmissions
There were several successful transmissions made and received between both Zane and Nikolai
However, many more packets were lost than were received
In the end, the long-range communication just wasn’t stable and reliable enough for demonstration purposes
16

## Slide 18: Final setup
Something more reliable
- Garage status can be viewed on mobile, tablet, PC
- Units send stall status to gateway from Zane’s house
Pi brokers MQTT topics and runs simulation; updates ESP32
ESP32 hosts a dynamic webpage showing active units, simulation
Gateway receives packets, sends to Raspberry Pi at Tyrel’s house
- Units read stall status
17

## Slide 19: Conclusion
Thank you for watching
18

## Slide 20: Park – it - cda
Questions?
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site
Sponsor/customer: Dr. John Shovic
Instructor: Dr. Frederick Sheldon