## Slide 1: Park – It - Cda
A Garage sensor system over a mesh network

## Slide 2: Value proposition
The problem
Too much time and effort are being spent by those looking for a place to park in one or more garages in downtown Coeur d’ Alene.
Our solution
A parking indication system
Vehicle sensing over stalls
LED indication to commuters
Mesh networking via detection/indication units

## Slide 3: Objective and deliverables
Our goal
Outfit the parking garage in downtown CDA with 5 prototype units
Build a mesh network for units to relay stall status to a gateway at the Innovation Den
Build a simulation to show what a full-garage deployment would look like

## Slide 4: Hard requirements
The units | The mesh network | The simulation
Enclosure no larger than 4” X 4” X 4” | Units relay messages to gateway at the den | representation of a full garage deployment
Sensors to detect presence of vehicles in stall | Data maintains integrity and authentication | Real time updates of stall status
Must last at least a year via battery power | Units are provisioned | Populated with accurate test data
LED to indicate stall status to commuters | Units are synchronized and can communicate with each other for message routing | Expandable for future projects
The units | The mesh network | The simulation
Redundancies of sensors for better accuracy | Units can choose a master and slave dynamically to save on battery | Graphical representation of system
Solar panels | Encryption of data | Companion app for phone/tablet
Security camera-like appearance for theft/tamper prevention |  | Data collection
soft requirements

## Slide 5: Park – it - cda
Team members and roles
Team leader
Mesh network
Nikolai Tiong
Zane Goodrick
Unit Design
Sensor Prototyping
Tyrel Parker
Simulation
Database
Joel Berain
Encryption
Wiki Site

## Slide 6: deliverables
Chart: 
| Testing | Design | Documentation
Breakdown of work | 0.2 | 0.3 | 0.5

## Slide 7: planning
Selecting hardware and software
Board qualities
- Low current usage for active and idle
- Enough memory to handle Radiohead library and sensor libraries
- 3v3 Power supply to save battery
Sensors and LEDs
- Deep sleep modes
- Accuracy
- Can interrupt processor
Mediums
- RGB LEDs for ease and enclosure space
- Low power, high range communication protocol
- Lightweight simulation software

## Slide 8: Components and mediums
The hardware
The Board
The Sensors
Other Components
Adafruit Feather M0 LoRa
RGB LED
AM312 PIR Sensor
HC-SR04 Ultrasonic Sensor
Locking Power Switch
Real-Time Clock
2500mah Lipo Battery
LoRa Antenna
Lipo Charger

## Slide 9: Sensing vehicles
- The ultrasonic sensor reads the distance to the ground 3 times to see if there is a blockage in the stall, outlying distances are thrown out in a 2 – to – 1 vote
A combination of sensors are used to detect the presence of a vehicle
- The PIR sensor wakes up the CPU via external interrupt when a heat signature (vehicle) is detected below
- The processor changes the LED from green (vacant) to red (full)
- Stall status is sent periodically to the gateway over LoRa transmission

## Slide 10: The Enclosure
Designing and 3d printing
Final enclosure design, created in Fusion360
Full assembly of working prototype
Copper PIR limiter
LED diffuser
Access to CPU and Lipo Underneath

## Slide 11: Trials and lessons learned
Sensors and enclosure

## Slide 12: Nikolai mesh networking
Font 48 for headlines
Font 36 for lists and other text

## Slide 13: Tyrel Simulation
Font 48 for headlines
Font 36 for lists and other text

## Slide 14: Joel Encryption
Font 48 for headlines
Font 36 for lists and other text
Encryption
A class was created to send and receive crypted data throughout the network. This
class implements private key cryptography.
      Two private keys and a predetermined pattern are used to encrypt and decrypt data
      Encryption method
      Methods to access or print the original and crypted data