Park-it-CDA

---
Team
- Nikolai
  - Mesh Networking
- Tyrel
  - Simulation
  - Database
- Zane
  - Unit design
  - Sensor prototyping

---
Requirements
- 5 Units
- 1 year battery life
- Sense obstacle
- Indicate blockage
- Mesh network
- Auto choose gateway
- Report state changes
- Simulate the rest of garage

---
Schedule

---
Assumptions
- We assume that LoRa will have the distance capabilities to reach the den.
- We assume that we can achieve everything on a 3.3v system.
- We assume that we can survive for a year on a 10000 mAh battery utilizing deep sleep.

---
Issues
- The battery life will be the bottleneck.
  - With a 3.7% PWM duty cycle on an arduino mega we can run the led for approximately 235 days with a 10000 mAh battery.
  - We assume that with a few solar panels we could extend the battery life to allow for a full year even with indirect lighting.
  - We could also blink the LED at regular intervals instead of having them on all the time. This requires timing between units.
  - We still need to allow for the networking.

---
Context Diagram

---
Context Diagram

---
Context Diagram

---
Impacted Modules
- We could purchase an off the shelf Arduino MKR 1310 which has a built in hardware encryption chip and 107uA deep sleep with built in LoRa.
- We would be relying on the open source LoRa libraries for our communication packages, and an open source package for the discreet simulator.

---
Three Prototype Test Cases
- Sensor
  - Identify a car, truck, and possibly a motorcycle
- Network
  - Mesh communication
  - External reporting
- Simulation
  - How do we test the simulation????

---
Traceability Approach
- "the ability to describe and follow the life of a requirement in both a forwards and backwards direction (i.e., from its origins, through its development and specification, to its subsequent deployment and use, and through periods of ongoing refinement and iteration in any of these phases)"
- We need to develop a way to show how this works.

---
Schedule

---
Current Status
We have ordered hardware and are waiting on some test items to arrive so we can test signal strength and power consumption.

---
Action Items
Intentionally left blank.